## Slide 1: 村松直哉
2018/8/2

## Slide 2: 書誌事項
Authors: Yoichi Ochiai, Takayuki Hoshi and Jun Rekimoto
Title: Pixie Dust: Graphics Generated by Levitated and Animated Objects in Computational Acoustic-potential Field
Journal:
  ACM Transactions on Graphics (TOG)
  Volume 33 Issue 4, July 2014
  Article No. 85
ISSN: 0730-0301
Pages: 85.1—85.13
Article Number: 85
URL: http://doi.acm.org/10.1145/2601097.2601118
DOI: 10.1145/2601097.2601118
要件：216 words

## Slide 3: 著者の抄録
We propose a novel graphics system based on the expansion of 3D acoustic-manipulation technology. In conventional research on acoustic levitation, small objects are trapped in the acoustic beams of standing waves. We expand this method by changing the distribution of the acoustic-potential field (APF). Using this technique, we can generate the graphics using levitated small objects. Our approach makes available many expressions, such as the expression by materials and non-digital appearance. These kinds of expressions are used in many applications, and we aim to combine them with digital controllability. In the current system, multiple particles are levitated together at 4.25-mm intervals. The spatial resolution of the position is 0.5 mm. Particles move at up to 72 cm/s. The allowable density of the material can be up to 7 g/cm3. For this study, we use three options of APF: 2D grid, high-speed movement, and combination with motion capture. These are used to realize floating screen or mid-air raster graphics, mid-air vector graphics, and interaction with levitated objects. This paper reports the details of the acoustic-potential field generator on the design, control, performance evaluation, and exploration of the application space. To discuss the various noncontact manipulation technologies in a unified manner, we introduce a concept called "computational potential field" (CPF).

## Slide 4: 自分の抄録
We propose a graphics system to control the spatial position and 3D animation of small objects by utilizing a noncontact manipulation technology.
Previous works on noncontact levitation/manipulation are based on potential fields determined by various physical quantities, such as sound pressure in acoustic levitation and magnetic fields in magnetic levitation. Levitated objects can be manipulated by spatially and temporally controlling the potential fields. When the field is controlled by a computer, we call it a “computational potential field” (CPF).
We present the details of system to control acoustic-potential field(APF) using ultrasonic-phased array and investigate the application of our system.
The organization of this contribution is as follows. First, we describe the design of our graphics system. We present the details of the ultrasonic-phased array and discuss its advantages and disadvantages. Second, we report the performance measurements of our system, including the measurements of the spatial resolution, stability, speed of movements, and size and weight of the levitated objects. Finally, we investigate the applications of our system. In addition to the examples of acoustic-potential field based graphics applications, we also discuss the implementation of 3D interaction. By integrating a motion-capture system into our graphics system, we facilitate interaction between the levitated objects and the user. Although our investigation is performed using acoustic levitation, our results and discussions can also be useful in designing other CPF-based graphics using other principles of mid-air levitation.

## Slide 5: 全体を通じての感想